## Slide 1: Developing Yellow Tail Kingfish Farming in Land-Based Closed-Containment Systems
Kees Kloet, Silt bv
Andries Kamstra, Wageningen-Imares
Aquacultuur symposium St-Niklaas, november 2013

## Slide 2: Content
Global status of Seriola farming
Rationale for YTK in RAS
Development of the project, Lab>Pilot>Commercial
System lay-out
Design parameters, water quality
Projected cost structure; competitive power
Marketing & Sales
Research & Prospects

## Slide 3
yellowtail kingfish, Seriola lalandi

## Slide 4: Global status of Seriola farming
9 species, 4 in aquaculture
130.000 tonnes production
80% Jap. amberjack
6 sites reproduction S. lalandi
Fish Base

## Slide 5: Rationale for YTK in RAS
Demand fresh product sushi/sashimi/carpaccio
Demand local product, certified and sustainable
Alternative for Tuna
Technology RAS developed
Fingerling production developed

## Slide 6: Development of the project
Start: project Fork to Farm 2009: lab-scale IMARES
  Water quality criteria
  Performance data
Pilot scale at farm with fish from IMARES
Start Silt 2011

## Slide 7: Lab-scale trials YTK
Replicated RAS
Very fast growth rate
FCR: 1.0
FCR: 0.7
growth

## Slide 8: Temperature
a
a
b
c
b
FCR: 1.13 1.11 0.98 0.88 1.00
Abbink et al.(2011). Aquaculture 330-33: p 130-135.

## Slide 9: pH
FCR: 1.26 0.98 0.91
35
a
b
b
Abbink et al.(2011). Aquaculture 330-33: p 130-135.

## Slide 10: Salinity
12
a
a
a
b
b
FCR: 0.77 0.76 0.77 0.81 0.82

## Slide 11: Feed

## Slide 12: Flow scheme Silt bv
to tanks
900 m3/h
O2
O3
To sludge storage
USB 30 m3
120 m3/d
14 x 27 m3
Drums, 40 micron
136 m3 Tricklingfilter
Bionet 200
Skimmer
70 m3/h
Upflow filters
40 m3
80 m3/h

## Slide 16: System performance
Design capacity 100 T/y
Max feed load realised: 450 kg/d = OK
Water use: 1000 l/kg feed (borehole 25 ppt)
Temperature: 21-24
TAN: 1.3 ± 0.8
NO2-N: 0.4 ± 0.2
NO3-N: 55.3 ± 11.1
pH>7.2
CO2 < 10 mg/l

## Slide 17: Economy: key numbers
100 T/Y, not reached
Desk study Aquavlan
1-2500 grams in 1 year
250 kg/m3/y
FCR 1.6
Investment 6,70 €/kg production
IRR 22%

## Slide 18: Projected cost structure

## Slide 19: Competitive power RAS vs Cages
RAS more expensive
RAS better certifiable
RAS for ‘local’ production
¥ vs €/$

## Slide 20: Marketing & Sales
Well received product
Applications: sushi/sashimi
Western-Europe, fresh round

## Slide 21: Depuration!
Marine RAS have off-flavour
  Turbot
  Kingfish
For YTK 2 days in make-up water
Awareness with all producers!

## Slide 22: Research & Prospects
Reproduction/breeding
On-growing diets
  Quality
  Reduction fish meal
Welfare,
  slaughter methods,
  water quality

## Slide 23
Thank you for your attention.
Questions?